## Slide 1: FAA AIRFIELD LIGHTING STANDARDS UPDATE
IES ALC - Fall Technology Meeting
Denver, CO
Oct 19, 2015
Tom Mai
FAA
Office of Safety and Standards
Airport Engineering Division (AAS-100)

## Slide 3: Agenda
FAA Plan &Spec Review
FAA Airfield Lighting Equipment Advisory Circulars (AC’s) & Engineering Briefs (EB’s) Published in FY 2015 (10/1/2014 to 9/30/2015)
FAA Airfield Lighting Equipment Draft AC’s & EB’s for FY 2016
FAA Significant Safety Issue (SSI)
Q & A
3

## Slide 4: FAA Review of Construction Plans and Specifications for AIP Funded Projects

## Slide 6: Background
2010 - FAA Review of Plans and Specifications (P&S) identified as a high value activity (HVA)
2011 – Business Plan Goal to setup team to work on standardization of P&S review
2012-2014 – ARP team developed a matrix template and checklists for reviews
Dec 2014 – Implementation memo signed by AAS-1

## Slide 7: Overview of Implementation Memo
Provides standardized guidance for all regions/ ADOs to use
Reviews required for AIP funded projects, encouraged for others
Risk based criteria to focus ARP resources on projects of higher dollar value, type of project and category of airport
Ensures compliance with standards and proper use of AIP funds

## Slide 8: Implementation Dates
Dec 8, 2014 – Program Managers (PMs)& Engineers encouraged to use Review Matrix and Review Guide for P&S reviews
Mar 1, 2015 –PMs & Engineers required to use Review Matrix and Review Guide for P&S reviews for AIP projects at Part 139 airports and AIP projects greater than $2M at GA airports
Oct 1, 2015 – PMs & Engineers required to use Review Matrix and Review Guide for P&S reviews on all AIP projects

## Slide 9: Objective of P&S Review by FAA
Check conformance to approved scope of work
Verify that work meets AIP eligibility and justification
Check conformance to FAA design and construction standards
  Looking for deficiencies as well as areas exceeding standards

## Slide 10: What the FAA P&S Review is Not
A quality control check for Engineer of Record
To validate technical engineering calculations
To give technical direction to Engineer of Record
To relieve Engineer of Record from professional duty related to P&S
An approval of any Mods of Standards

## Slide 11: Determine Level of Review
No Review (Sponsor Certification)
General Review
Full Review
Based upon:
Type of project
Type of airport (Part 139/Primary) or Non-Primary
Total est. construction or equipment cost

## Slide 14: P&S- Side Notes
A brief overview on early findings for P&S reviews with regard to MOS and MOS for State Specifications that some regions finding no MOS for changes to specifications.
State standard for airport projects versus state specifications for individual projects
Legislation permits FAA to allow sponsors to use state specifications but that does not mean it may not require a MOS
12,500 state specifications no MOS
<12,500 and < 60,000 require a MOS for P401, P403 and P501 unless for non aeronautical pavement or shoulders

## Slide 15: AC’s & EB’s PUBLISHED IN FY 2015
AC 5345-53C Airport Lighting Equipment Certification Program (Addendum is updated monthly)
AC 150/5345-44K, Specification for Runway and Taxiway Signs (10/8/2015)
AC 150/5345-42G, Specification for Airport Light Bases, Transformer Housings, Junction Boxes, and Accessories (Legal review)
AC 150/5345-46E, Specification for Runway and Taxiway Light Fixtures (Legal Review)
AC 150/5345-49D, Specification L-854, Radio Control Equipment (Legal Review)
EB No. 93, Guidance for the Assembly and Installation of Temporary Orange Signs (Ready to be published)

## Slide 16: AC 150/5345-44K, Specification for Runway and Taxiway Signs
1. Paragraph 1.1, reference to dot matrix signs removed.
2. Paragraph 1.2.1, the Note about a black outline for the letter “M” is removed from and moved to Appendix I, Figure 19.
3. Paragraph 1.2.1, subparagraph e about dot matrix signs is removed
4. Paragraph 1.2.4e – sign shipping and storage temperature requirements are removed because they are stated in paragraph 3.2.1, Sign Temperature Requirements.
5. Paragraph 1.2.6 – paragraph is clarified with redundant statements removed. The Note is deleted and added to the paragraph as 1.2.6b4.
6. Paragraph 1.2.6 – message array definition added. Sign frame definition added. Sign array definition added.
7. Paragraph 1.2.6.i is added to define a sign array.
8. Paragraph 3.2.1 – a reference to the appropriate testing paragraph is added. Sign temperature requirements are modified to accommodate LEDs.
9. Paragraph 3.2.2 – Reference to testing section applicable paragraphs is added. The Note is deleted and added to the paragraph as 3.2.2d.

## Slide 17: AC 150/5345-44K, Specification for Runway and Taxiway Signs (Cont.)
10. Paragraphs 3.2.3 – paragraph references to Section 4 are added.
11. Paragraph 3.2.5.1 – stake mounted signs are deleted within lighted sign requirements.
12. Paragraph 3.2.5.2 – message element spacing is added for sign sizes.
13. Paragraph 3.2.5.2, Table 1, Note 4 is added for unlighted signs.
14. Paragraph 3.2.5.4b is updated to be inclusive of all applicable requirements in the ASTM 4956, Standard Specification for Retroreflective Sheeting for Traffic Control.
15. Paragraph 3.2.5.4.2 – Note is removed and added as paragraph 3.2.5.4.2c
16. Paragraph 3.2.5.6c is deleted because it is previously mentioned in paragraph 3.2.5.1c
17. Paragraph 3.2.5.12e is added because the Note is deleted.
18. Paragraph 3.2.5.14d is removed because the requirement is already stated in paragraph 3.2.5.11c.
19. Paragraph 3.2.6.2 is updated to be inclusive of all applicable requirements in the ASTM 4956, Standard Specification for Retroreflective Sheeting for Traffic Control.
20. Paragraph 3.2.6.5 – the exception is removed from the beginning and placed as a NOTE at the end of the paragraph.

## Slide 18: AC 150/5345-44K, Specification for Runway and Taxiway Signs (Cont.)
21. Paragraph 3.2.6.11 – Instruction Booklet is made consistent for lighted and unlighted signs. Sign maintenance instructions are added
22. Paragraph 4.1.1.1b is clarified for L-858R signs.
23. Paragraph 4.1.1.1f is deleted because it repeats what is stated in subparagraph i.
24. Paragraph 4.1.1.1k – expected results for the test is added.
25. Paragraph 4.1.1.2, Note 4 is updated to better define testing requirements for curved sign faces.
26. Paragraph 4.1.1.3.1, IESNA document title added for clarity.
27. Paragraph 4.1.1.3.3, L-858B and L858H signs are removed from photometry tests.
28. Paragraph 4.1.1.3.4, NOTE is removed for dot matrix signs.
29. Paragraph 4.1.1.9 is updated for power factor test conditions that are consistent with other ACs.
30. Section 6, Dot Matrix Signage, is removed along with all references throughout the AC.
31. All Figures are updated to a standard format.
32. Figure 5, Note c is clarified.
33. Table 5 is updated to remove ALPHA characters for size 4 signs.
34. Table 6 is updated to remove ALPHA characters for size 5 signs.
35. Figure 14, dot matrix references are removed.
36. Figure 17, an additional note is added to clarify the sign face.
37. Numerous grammatical and format changes made throughout the AC.
38. All references and any associated Uniform Resource Locators (URLs) are updated.

## Slide 19: 150/5345-42H DRAFT, Specification for Airport Light Bases, Transformer Housings, Junction Boxes, and Accessories
Para 3.2.3.1, elevated light base plates are removed from AC 150/5345-46, Specification for Runway and Taxiway Light Fixtures, and added to this AC to facilitate common hardware in one AC.
Para 3.2.3.1.1 through 3.2.3.1.4 are added to describe elevated light base plate requirements.
Para 3.2.3.2 is added to include elevated light fixture mounting stakes with common hardware.
Para 3.2.3.2.1 through 3.2.3.2.6 are added to describe elevated light mounting stake requirements.
Para 4.2.8 is a added to provide test procedures for elevated light base plates.
Figures 6 & 7 “AAA” dimension and is changed in both figures for manufacturing uniformity among one piece and sectional light bases.
Figure 7 – AAA dimension tolerance is changed to match the tolerance in Figure 6 for better uniformity.
Notes: Currently, elevated light baseplates are certified as part of the light since the requirements are found in FAA AC 150/5345-46D.
Baseplates do not have their own “L” designation like other similar equipment found in FAA AC 150/5345-42G.
When elevated lights are certified, they are done so with a particular baseplate.

## Slide 20: 150/5345-46E DRAFT, Specification for Runway and Taxiway Light Fixtures
“FAA Type” L’s fixtures added throughout the AC
Para 3.4.1.1, Class 1 (Direct Mounted), is rearranged for clarity
Para 3.4.1.2d is changed to allow deeper throat projection of light fixtures. This solves potential issues with light fixtures not fitting through the bottom flange cutout of existing extensions and sectional light bases.
Para 3.4.2.2, Base Mounting, Elevated light fixture base mountings are removed from the AC and placed in AC 150/5345-42, Specification for Airport Light Bases, Transformer Housings, Junction Boxes, and Accessories, to consolidate all light bases into a common document.
Para 3.4.2.3, Stake Mounting, Elevated light stake mountings are removed from the AC and placed in AC 150/5345-42.
Para 3.7.2.d, revised for clarification
Para 3.7.2.1, Mode 1 (Series Powered) Fixtures is rewritten for clarity
Para 3.10.1.1 is rewritten to clarify the requirement for light fixture internal hardware. The requirement for black oxide coatings is removed. A note is added about in-pavement light fixture bolts and bolt torque requirements.
Notes: Classes-apply to in-pavement fixtures
Class 1-directed mounted fixtures
Class 2-base-mounted fixtures
3.4.1.1d applies to Chass 2 only. “Any projection of the light fixture beyond the ¼ inch throat projection must be sized to fit through a multiple section light base (bottom/middle & bottom flange of the top section)

## Slide 21: AC 150/5345-49D DRAFT, Specification L-854, Radio Control Equipment
Change low end of environmental temperature range from -67° F (-55° C) to -40° F (-40° C) for better parts availability.
Paragraph 3.4.3b(1) – delete operation of the Type II Receiver at 450 – 512 MHz due to no currently certified manufacturers.
FAA Spectrum Management currently deliberating with NTIA about 450 -512 MHz band use.

## Slide 22: ENGINEERING BRIEF No. 93 Guidance for the Assembly and Installation of Temporary Orange Signs During Construction
This Engineering Brief (EB) provides guidance about materials, and methods of assembly and installation of temporary orange construction signs.

## Slide 23: Draft AC’s & EB’s for FY 2016
AC 150/5345-43H, Specification For Obstruction Lighting Equipment
AC 150/5340-18G, Standards for Airport Sign Systems
AC 150/5340-30J, Design and Installation Details for Airport Visual Aids
AC 150/5370-2G, Operational Safety on Airports During Construction
Engineering Brief No XX– PAPI
EB 92, Light Spacing Guidance for New Taxiway Fillet Geometry, Rev 1

## Slide 24: DRAFT AC 150/5345-43H, Specification For Obstruction Lighting Equipment

## Slide 26: DRAFT AC 150/5345-43H, Specification For Obstruction Lighting Equipment
Update to include new “Flashing” L-810 to meet new requirements in a draft AC 70/7460-1L
DRAFT AC 70/7460-1L, Chapter 5 “….Flashing Lights (L-810). For structures exceeding 151 feet (46 m) but not more than 350 feet (107 m) at intermediate levels, two or more flashing (L-810) lights should be mounted outside at diagonally opposite positions of intermediate levels. These lights should be configured to flash simultaneously with the L-864 flashing light on the top of the structure at a rate of 30 flashes per minute (fpm) (± 3 fpm).
Published by CY 2015.

## Slide 27: Proposed changes to AC 150/5345-43H
Flashing L-810 (F) 30 FPM (± 3 FPM) or (± ?%)
Synchronization
  Flash duration?
  Start up time?
  Be mated with exiting L-864 or dual L-864/865 controller?
  Controller requirements included/modified?
  Would flashing affect the performance of L-810?
  Light output: Determine effective intensity or steady evaluation of 32.5cd is sufficient?
  Testing requirements?
L-864 flash rate changes to 30 FPM?

## Slide 28: AC 5340-18G Draft, Standards for Airport Sign Systems-Principal Changes
Incorporate EB 89, Clarifications of Taxiway Nomenclature
Introduce new “Approach” signs
Introduce “new” Orange Construction signs
Update drawings
Clarifications with examples

## Slide 29: Current
Proposed

## Slide 31: Draft AC 5340-18G- New Proposed Signs

## Slide 32: Draft AC 150/5340-30J, Design and Installation Details for Airport Visual Aids
Update reference to runway guard light intensity requirements. Reference AC 150/5345-46 rather than attempting to paraphrase.
Update/check all referenced documents in the AC.
Clarifications
Update some figures

## Slide 33: Wind Cone and L-810 Issue FAA AC 150/5340-30H, Par. 6.7.2.e
This states:
Note: Power for obstruction lights mounted on wind cone structures must be on a dedicated circuit not shared with other equipment. This assures continued lighting of the obstruction in the event of a runway lighting power failure.
More brush block contacts would be needed in order to implement a dedicated circuit
This currently is not available

## Slide 34: UPDATE Wind Cone and L-810 Issue FAA AC 150/5340-30H, Par. 6.7.2.e
Propose the following clarification in the next -30
“The intent of the Note in Paragraph 6.7.2.e in AC 150/5340-30H is that the obstruction lights on top of the wind cone must be lighted even if the runway edge lights are shut down. The obstruction lights can be powered from a dedicated circuit, or shared with another circuit such as a runway sign circuit as long as the obstruction lights have power available even if the runway lights are shut down.”
For clarification, we will revise the Note in the next revision of AC 150/5340-30J to read as below:
“Note: Power for obstruction lights mounted on wind cone structures must be on a circuit not shared with runway lights or other circuits that maybe shut down for operational closures. This assures continued lighting of the obstruction in the event of a runway lighting shutdown during closure or maintenance.”

## Slide 35: EB No. 92 Rev. 1, Light Spacing Guidance for New Taxiway Fillet Geometry Per AC 150/5300-13A, Change 1, Airport Design.
This EB introduces guidance and new requirements for edge lighting the new taxiway fillet geometries designed for cockpit over centerline rather than the judgmental over steer currently used throughout the NAS. The EB provides proposed design examples that show proposed edge light layouts.

## Slide 38: Draft EB- PAPI
Engineering Brief - disseminate additional information about how PAPI Obstruction Clearance Surfaces (OCS) are evaluated by FAA Flight Inspection. In addition, provide information about how to deal with obstructions that are outside the 20 degrees PAPI OCS imaginary plane.

## Slide 39: FAA SSIs
Definition: Cross organizational issues that have potential to be identified as high risk.

## Slide 41: FAA SSIs
“LED Lighting of Airfields, Obstacles, and Aircraft” is #1 of the top 10 list for full SRM
Stakeholders: ATO, AVS, ARP
OPR

## Slide 43: Q & A
43
Notes: 43

## Slide 44: Thank You!
44
Notes: 44