## Slide 1
Federal Aviation
Administration
Illuminating Engineering Society (IES) Government Contacts
Sub-Committee Meeting
Navigation Programs,
Lighting Systems Sub-Team
AJM-3222
October 19, 2015

## Slide 2: Overview
Organizational Structure
Lighting Systems
Navigation Roadmap
Advanced Lighting Concepts
Active Projects
Specification Updates
Procurement Opportunities

## Slide 3: Program Management Organization (AJM-0)

## Slide 4: Enterprise Services

## Slide 5: Lighting Systems

## Slide 6: Lighting Systems and Ancillary Equipment
High Intensity Approach Lighting System with Sequenced Flashing Lights (ALSF-2)
Medium Intensity Approach Lighting System with Runway Alignment Indicator Lights (MALSR)
Precision Approach Path Indicator (PAPI)
Runway Visual Range (RVR)
Runway End Identifier Lights (REILs)
Radio Remote Control System (RRCS)
Radio Remote Control Interface Unit (RRCIU)
Replacement Lamp Monitoring System (RLMS)
Lead-in Lights
Semiflush Flashers & Steady Burners
Low Impact Resistant (LIR) Structures
Transformers
Frangible Bolts
Aiming Devices

## Slide 7: Navigation Roadmap

## Slide 8: Navigation Roadmap
The NAS Navigation Strategy provides information for the sustainment of current navigation services, the transition to performance-based navigation (PBN), and the delivery of the Next Generation Air Transportation System (NextGen) services.
It addresses the planning and actions required through the 2025 - 2028 timeframe.

## Slide 9
Notes: Navigation Program Evolution
Today
  NAS navigation services are based on a combination of ground-based and satellite-based services in all phases of flight
  PBN capabilities have been initiated in the NAS
Future
  Navigation will continue to be based on a combination of ground based and satellite based services in all phases of flight
    The ground based navaids (GBN) infrastructure will be reduced
  Navigation will be primarily provided by satellite based systems
  Advanced Lighting Concepts will be needed in the future

## Slide 12: Advanced Lighting Concepts
LED MALSR
LED PAPI
LED ALSF-2
LED REIL

## Slide 13: MALSR Initiatives
Service Description
The MALSR provides visual information on runway alignment, height perception, roll guidance, and horizontal references for Category (CAT) I precision approaches and Special Authorization CAT II Operations
Roadmap to the future
Transition from current PAR-38 incandescent lamps to energy efficient LED technology
  Developing alternative LED lamps that can use existing lamp fixtures to minimize cost of conversion
  Establish a transition plan to replace incandescent lamps
  Determining need to retain some infra-red emission to support enhanced flight vision systems (EFVS) and Night Vision Systems (NVS)
Transition from current PAR-56 threshold lamps to LED technology
  Rely on LED technology to improve reliability and maintainability and reduce ops costs

## Slide 14: ALSF-2 Initiative
Service Description
The ALSF-2 provides visual information on runway alignment, height perception, roll guidance, and horizontal reference for all categories of precision approaches, primarily Category (CAT) II/III
Roadmap to the Future
Evaluate potential for reducing footprint and number of lamps needed to support CAT II/III approaches
Leverage lessons learned from the MALSR program to implement Light Emitting Diode (LED) in the ALSF-2 design to the extent possible

## Slide 15: PAPI Initiative
Service Description
PAPI provides visual approach slope information to pilots and enables them to make stabilized descent and approach clearances over obstructions
  PAPI is used primarily to support Visual Flight Rules (VFR) operations
Roadmap to the future
  Insert LED technology into legacy lighting systems that addresses improving reliability and maintainability
    Possible to reduce the lifecycle cost of Visual Glide Slope Indicator (VGSI) by at least 50 percent

## Slide 16: REILs Initiative
Service Description
The REIL is a non-precision visual aid that provides rapid and positive identification of the approach end of a particular runway to the pilot.
REILs are required for current and future NAS operations
Approx. 400 REILS are beyond their 20 year life-cycle; over 200 REILs are >30 years old
Roadmap to the future
Transition from zenon flashtubes to LED Technology
Insert LED technology into legacy lighting systems to improve reliability and maintainability
Current program is replacing REILs to at a rate of ~10/year

## Slide 17
Service Description
  Runway Visual Range (RVR) provides air traffic controllers with a measure of the distance a pilot can expect to see the runway
  RVR becomes critical when visibility is less than a mile
  RVR information is required for departure and Category (CAT) II, III, and many CAT I precision approaches
Roadmap to the Future
  RVRs are required for the current and future NAS operations to:
    Replace aging transmissometers and non-PC-based systems
    Support future precision approach requirements
RVR Initiative
RVR

## Slide 18: Lighting Systems Future Initiatives
ALSF-2/MALSR: Conduct Analysis on the feasibility of reducing the footprints of these lighting systems
Redesign MALSR system based on LED technology
Redesign ALSF-2 system based on LED technology

## Slide 19: Active Projects

## Slide 20: Active Project List
Background on LED Projects
LED PAPI
LED MALSR PAR-38 Replacement Lamp Project

## Slide 21: Background on LED Project

## Slide 22: LED Issues
FAA Significant Safety Issues
  FAA’s top safety related issue is LED Lighting on Airfield, Obstacles and Aircraft
    Pilots using Night Vision Goggles (NVG) or Enhanced Flight Vision Systems (EFVS) lack ability to see LEDs
    Unmanned Aircraft Systems sensors have limited or no ability to sense LED’s
    Pilots concern about glare from high intensity LED’s on taxiways and runways off haze, fog, low ceiling cloud decks…
  Establish Team to Conduct Safety Risk Management (SRM) panel
    A cross-organizational approach to conduct SRM
LED Moratorium
  Office of Airports has issued a moratorium on High Intensity Runway Edge Lights (HIRLs)

## Slide 23: LED Symposium
Objective:
  Focus is on Approach Lighting and Airport Lighting
  Identify needed Areas of Research and Testing
  Achieve Collaboration from Stakeholders
  Establish Plan of Action and Timelines
  Fix It!
Participants:
  Industry: ALPA, Pilots, Lighting Experts, FEDEX
  FAA: Navigation Programs, Airports, Tech Center, Flight Standards, CAMI, Volpe
Outcome:
  Established Three (3) Groups
    Science, Infrastructure and Operational

## Slide 24: Next Steps
Work with Stakeholders and FAA to identify resources needed to continue evaluation of LED Technology
  Conduct additional research on LED’s
    Brightness, Glare
  Conduct Operational Test on LED’s
    Clear, Rain, Snow, Fog
  Establish a Safety Panel specifically on LED’s
Revalidate Lighting Requirements
  Intensity Steps
  Photometrics
  Brightness
LED issues have impacted LED Projects

## Slide 25: LED PAPI

## Slide 26: LED PAPI Project
Objective: The primary objective is to fully deploy LED PAPI by using the System Development, Deployment and Implementation phases of FAA’s Acquisition Management Systems (FAMS) process.
  Project Activities
    Preliminary Design Review
    Critical Design Review
    Design Qualification Test
    Operational Test
    Configuration Audits
    Product Baseline
    Deployment

## Slide 27: LED PAPI Project Impacts
Extensive Safety Review
  Conducted several Safety Risk Panel meetings to identify potential hazard conditions involving visual guidance indicators
Additional Flight Evaluations
  Conducted video recording of LED PAPI, incandescent PAPI and Visual Approach Slope Indicator at key-site Vero Beach, FL (VRB) - September 2014
  Conducted Flight Demonstration at Vero Beach, FL with Flight Standards to resolve brightness perception - December 2014
  Conducted another Flight Demonstration at Vero Beach, FL - June 2015

## Slide 28: Flight Demonstration
Objective:
  To resolve any questions about brightness perceptions of a LED’s PAPI systems
  Confirm accurate glide slope guidance
  Capture any effects caused by haze or fog
  Confirm the LED PAPI does not contribute to the loss of a pilot’s situational awareness or cause any distractions
  Comparison of LED PAPI and Incandescent PAPI
Observation:
  Global Brightness
  Global Blooming
  Brightness Directional Stability
  Color
  Color Stability
  Transitioning/Trending
Vero Beach LED PAPI Video September 2014 V3.mov

## Slide 29: Flight Demonstration (December 2014) Results
 | Global Brightness | Global Blooming | Brightness Directional Stability | Color | Color Stability | Transitioning/Trending
Day | 2 | 2 | 3 | 1 | 1 | 2
Twilight | 2 | 2 | 3 | 1 | 1 | 2
Night | 3 | 3 | 3 | 1 | 1 | 2
Dawn | 2 | 2 | 3 | 1 | 1 | 2
1 - Excellent, highly desirable
2 - Good, negligible deficiencies
3 - Fair, some mildly unpleasant deficiencies
4 - Minor but annoying deficiencies
5 – Moderately objectionable deficiencies
6 – Very objectionable but tolerable deficiencies
7 - Major deficiencies
8 - Major deficiencies
9 - Major deficiencies
10 – Major deficiencies
Lighting Acceptability Rating Scale (LARS)

## Slide 30: Flight Demonstration (December 2014) Results
Summary/Recommendations
  LED PAPI is satisfactory under the conditions we saw during this demonstration
  The transitioning or trending information was good
  The best feature of the LED PAPI is its sharp, vivid colors
  The white was excellent and a major improvement over the incandescent
  The brightness was not overwhelming nor did lead to a loss of situational awareness
  The increased brightness was more noticeable at night
  More data points on this system in its entire operational environment will be very beneficial going forward

## Slide 31: Flight Demonstration (June 2015) Results
 | Global Brightness | Global Blooming | Brightness Directional Stability | Color | Color Stability | Transitioning/Trending
Day | 1 |  |  | 1 |  | 1
Twilight | 1 |  |  | 1 |  | 1
Night | 1 |  |  | 1 |  | 1
Dawn | N/A |  |  | N/A |  | N/A
1 - Excellent, highly desirable
2 - Good, negligible deficiencies
3 - Fair, some mildly unpleasant deficiencies
4 - Minor but annoying deficiencies
5 – Moderately objectionable deficiencies
6 – Very objectionable but tolerable deficiencies
7 - Major deficiencies
8 - Major deficiencies
9 - Major deficiencies
10 – Major deficiencies
Lighting Acceptability Rating Scale (LARS)

## Slide 32: Flight Demonstration (June 2015) Results
Comments
  Rwy 4 (LED)
  (Day) Excellent Visibility/Brightness from 5 miles
  (Dusk) Excellent Visibility/Brightness from 5 miles, excellent transition
  (Night) Did not wash out runway, noticeable at 20nm and 5500 ft.
  Rwy 12R (Incandescent)
  (Day) Hard to discern for 2 miles
  (Dusk) Good brightness/intensity noticed at 5nm, good transition
  (Night) Same as dusk except lights seem to wash out runway.

## Slide 33: LED PAPI Project
Planned Activities
Complete LED PAPI standard installation drawings – December 2015
Establish System Baseline – March 2016
Obtain ISD/Deployment Decision – June 2016
Commission key site at Vero Beach Municipal Airport (VRB) in Vero Beach, FL – June 2016

## Slide 34: LED PAPI Project
Planned Activities
Implementation Activities
  Rochester International Airport Runway 22, Rochester, NY
  Flagstaff Pulliam Airport Runway 03, Flagstaff, AZ
  Valley International Airport Runway 35L, Harlingen, TX

## Slide 35: MALSR LED PAR-38 Replacement Lamp Project

## Slide 36: MALSR LED PAR-38 Replacement Lamp Project
Objective: Determine the I/R requirements for a PAR-38 LED replacement lamp. This will includes a feasibility study, developing requirements and evaluating the concept by prototyping, testing and conducting operational capabilities demonstrations.
  Phase I:
    Feasibility Study
      To determine if integrating IR into a LED Par 38 and Par 56 fixtures is achievable.
  Phase II:
    Prototype Development
    Confidence Testing
    Pre-Flight Testing
    Operational Capability Demonstration (OCD) with EFVS-equipped aircraft
  Phase III:
    Production

## Slide 37: Test Activities
Confidence Test
Pre-Flight Test
Flight Test (OCD) & Duration Testing (Volpe)
Validate “numbers” to ensure we are in the same ballpark and that technologies are compatible under simulated low-visibility conditions
Consists of “Laboratory” and/or “Field” testing
Ensure “look-and-feel” is validated before committing to flight
Formal Flight Testing –chasing “relevant” wx will prove challenging
Continue “static” weather related testing to supplement flight testing
Photometric and EVS testing
Accomplish the “easy” stuff before tackling the weather!

## Slide 38: Milestone Schedule
Confidence
Completed
9/2012
Pre-Flight
Completed
1/2015
Duration Testing
Not Started
OCD/Flight
Completed
5/2015

## Slide 39: Confidence Test
  EVS Ground Testing
  What: Test the cameras’ ability to image the lamps in quantities of digital units, pixels and analysis of the images for the documented EVS camera test settings in a laboratory test environment at short range.
  Where: Kollsman Facility (Merrimack, NH)
  When: August 7th ,8th, and 9th 2012
  Results: Determined EVS cameras can image LED’simage the LED/IR Lamps

## Slide 40: EVS Camera Test Results

## Slide 41: Confidence Test
  FAA Photometric Testing
  What: PRD 4.4.3.2: Measure average intensity, maximum intensity, chromaticity
  Where: FAA Technical Center (Atlantic City, NJ)
  When: August 14th, 15th, & 16th, 2012
  Results: Validated Requirements PRD) requirements are achievable
Pattern | Steady Burning Average Intensity (Candela) |  | 
 | Low (4%) | Medium (20%) | High (100%)
Main Beam (±8°) | 400 ± 60 | 2,000 ± 300 | 10,000 ± 1500

## Slide 42: FAA Photometric Test
8 Deg +-
5 Deg +-
Meets Minimum
Average = 9372 cd
Maximum = 13180 cd

## Slide 43: Confidence Test Conclusions
Photometric requirements were met
EVS Cameras displayed LED Prototype images on monitor
LED Prototype IR were still visible through Neutral Density filters as high as 3.5 OD - equivalent to 0.0316% transmission of signal to camera
Test Results (Photometric, Radiometer and EVS Camera) were encouraging

## Slide 44: Pre-Flight Testing
Consists of “Laboratory” and/or “Field” testing
Accomplish the “easy” stuff before tackling the weather!
Ensure “look-and-feel” is validated before committing to flight

## Slide 45: Pre-Flight Results
Test | Results
Photometric | Pass
Relative Intensity at Temperature | Pass
Chromaticity | Pass
Power Interruption | Pass
Voltage Variation | Pass
Voltage Harmonic | Pass
Current Harmonic | Pass
Power Factor | Pass
Grounding and Bonding | Future Validation
Power Line Surge | Future Validation
Test | Results
Environmental | Pass
LED Circuitry | Pass
Solar Radiation | Future Validation
Conducted Emissions (CE101) | Pass
Conducted Susceptibility (CS101) | Pass
Radiated Emissions | Future Validation
Radiated Susceptibility | Pass
Conducted Emissions (CE102) | Future Validation
Conducted Susceptibility (CS114) | Pass
Electrostatic Discharge | Pass

## Slide 46: OCD (Flight Test)
Formal Flight Testing
  Chasing “relevant” weather will prove challenging
Requirement Verification and data gather effort
  Current applications, standards, and specifications to demonstrate overall NAS operational capability

## Slide 47: OCD (Flight Test)
Incandescent MALSR 200FT AGL

## Slide 48: OCD (Flight Test)
LED MALSR 200FT AGL

## Slide 49: OCD Recommendations
Incorporate the brightness/luminance factor for LED lamps on Medium and Low intensities.
Define and agree on operational requirements for implementing IR into LED lamps.
  How much IR is needed to fully image approach lights on current EFVS Heads-Up Displays (HUDs)?
  What are the operational and performance parameters for IR?
  Should identical levels of IR be the same for LEDs as with incandescent bulbs?
Use cast-iron lamp holder (FA-11506 or equivalent) for LED MALSR Systems

## Slide 50: OCD Recommendations
Update ALS infrastructure for WJHTC experimental MALSR to make standard MALSR.
  Are current conduits, structures, and cabling techniques adequate for implementing newer LED MALSRs at airports.
Re-evaluate Electromagnetic Interference (EMI) requirements of LED lamps for use in the NAS.
Further research and evaluate the validity of PRD requirements that were not successfully validated or verified through the OCD.
  Are the requirements for which LED prototypes did not meet still valid?
  What changes (if any) need to be made to the requirements as written?
  Can LED prototype lamps be further optimized to meet all requirements?
.

## Slide 51: OCD Recommendations
Evaluate green threshold LEDs for use in a full MALSR
  Are there any functional, performance, or operational impacts with the implementation of green LED lamps
Provide funding to continue all LED activities and objectives including defining a minimum IR requirement)
  Continue research and validation activities on all Future Verification (FV) requirements in the VRTM.

## Slide 52: LED PAR-38 Replacement Project Summary
LED PAR-38 met majority of requirements in our LED Performance Requirements Document (LED-PRD-001)
  Photometrics
  Chromaticity
Seven (7) flights were conducted during clear weather
Without weather could not validate if LED’s with IR is sufficient for EFVS operations during Category I weather
  Very encouraged with results even without weather

## Slide 53: LED PAR-38 Replacement Project
Planned Activities
  Upgrade MALSR system at FAA Technical Center (ACY Runway 4)
  Incorporate Brightness/Luminous Ratio of 1.6 for Medium and Low Intensity step
  Work with LED Symposium Test Group to define testing requirements for LED approach lights
  Plan Flight Test activities with LED Symposium Test Group

## Slide 54: Other Lighting Projects
LVICC
RLMS
Semi-Flush Flasher
RRCS

## Slide 55: Replacement Lamp Monitoring System (RLMS)
Objective:
  To replace the constant current regulators and implement lamp monitoring on the Airflow and Godfrey ALSF-2 systems.
Status:
  Complete deliveries, which include RLMS kits, kits installations and RLMS power supplies
  RLMS contract closeout
  Install six (6) RLMS kits at various locations

## Slide 56: Semi-Flush Flasher Light Unit (SFFLU)
Objective:
  To develop and approve a semiflush flashers light unit through the FAA’s Developmental Hardware Process.
Status:
  Completed Development Test
  Completed Operational Test
  Installed SFFLU at various locations
    Alliance, TX
    Flagstaff, AZ
    San Jose, CA
  Approve product baseline

## Slide 57: Low-Voltage Individual Control Cabinet (LVICC)
Objective:
  To develop and approve an ICC that reduces the voltage from 2000V to 400V and interfaces with semiflush flashers. LVICC is compatible with MALSR and ALSF-2 systems
Status:
  Completed Operational Test
  Updated MALSR and ALSF-2 product baseline
  Installed at various locations
    Flagstaff, AZ
    San Jose, CA
    Long Beach, CA
  Finalize training material for technicians

## Slide 58: Specification and Procurement Opportunities

## Slide 59: Specification Updates
RVR Specification
  Anticipated Approval (December 2015)
Radio Remote Control System
  Anticipated Approval (January 2016)
REIL Specification
  Anticipated Approval (July 2016)
MALSR Specification
  Upcoming
In-pavement Steady-Burner Specification
  Upcoming

## Slide 60: Procurement Forecast
Remote Radio Control System (RRCS)
Remote Radio Control Interface Units (RRCIU)
Runway Edge Identifier Lights (REIL)
You should continue to monitor the FAA Contracting Opportunities Website for procurement opportunities
FAA Contracting Opportunities website: https://faaco.faa.gov/

## Slide 61: Questions

## Slide 62: Lighting Systems Team Contact Information
Name | Projects | Phone
John Varas | Manager | 202.267.4539
Renee Williams | RVR, LEDs, LIR | 202.267.9923
Ndubuisi Nnorom | RRCS, RLMS, Semiflush Flashers | 202.267.9883
Andrea Scott | RRCIU, MALSR | 202.267.4890
Kevin Teel | RLMS, RRCIU | 202.267.3444
Patrick Eigbe | REIL | 609.485.7857
Donald Lampkins | MALSR, PAPI, LEDs | 202.267.7332