## Slide 1
IES-RP-37-15:
Outdoor Lighting for Airport Environments
A New Recommended Practice for the Aviation Community
Authored by:
The IES Aviation Lighting Committee
2017 IESALC Fall Technology Meeting
October 23, 2017
John J. Wujek, PE
Notes: Welcome to the final day of the Hershsey Airport Conference. This morning I will discuss RP-37. An Illuminating Engineering Society Recommended Practice for airports. How I was developed, its purpose and how to apply it.
Following this presentation will be a case study for lighting presented by Carl Johnson and Jeff May.

## Slide 2: Why RP-37?
2005 IES-ALC formed the sub-committee for Recommended Practice to update the old RP-14-87
The IES RP-37 sub-committee is comprised of :
  Airports
  Manufacturers
  Designers
  Contractors
Sub-Committee members included:
  Richard Larivee, Sub, Chair
  Fred Loeffler, Vice –Chair
  John Wujek, Secretary
  E. Alf
  Carl Johnson
  H.C. Johnson
  H. McKee
  A. Seiterle
  Irwin Smiley
  M. Tebeau
  C. Twibell

## Slide 3: Why RP-37?
The IES RP-37 was preceded by RP-14-87 from 1987. The old RP provided good general information but………
Where do you put the light on the apron?
How much light on the apron?
What defines the apron?
These questions and the need to educate new personnel to the airport environment with respect to lighting design provided the spark to develop RP-37.

## Slide 4: Why RP-37?
Several Airport authorities and organizations have provided some guidance on the location and quantity of lighting at airports over the years.
ICAO
FAA
IES
CASA
All varying standards and recommendations on Lighting…….So,

## Slide 5: Why RP-37?
To cover the entire Airport Environment it was evident that the committee needed to provide a Recommended Practice that:
  Defined the areas on the airside and landside
  Describe the activities and operations that occur in these areas
  Describe and define the visual issues specific to the airport environment
  Define the design criteria for the airport areas
  Provide reference to other standards, RPs, Aviation Authority documents

## Slide 6: Contents
The content for the RP includes:
  Introduction
  Characteristics of Airport Areas
  Visual Issues
  Design Criteria
  Essential Safety and Security Lighting
  Environmental Considerations
  Annexes A through I for supporting
  Documentation
  Lets get started!

## Slide 7: 1.0 Introduction
This IES Recommended Practice provides guidance to provide an adequate and safe lighted environment while emphasizing restrictions, regulations and best practices for:
  Aircraft servicing and apron areas
  Aircraft support services, i.e., fueling, cargo, baggage load/unload
  Passenger loading and unloading
  Roadways
  Vehicle parking facilities
  Pedestrian walkways
The RP Encompasses the entire Airport Environment, both Airside and Landside.

## Slide 8: 2.0 Characteristics of Airport Areas
This section defines the activities and operations on the Airport:
  Aprons; Commercial (Air Carrier), Cargo, Hangar, General Aviation
    Aircraft Stand
    Aircraft parked position
    Aircraft service area
  Other Airside Areas
    De-icing Facilities
    Fuel Facilities
    GSE Storage Areas
    Engine Run-up / Test Areas

## Slide 9: 2.0 Characteristics of Airport Areas
Aprons:
  General Layout shown
    Parking aircraft
    Aircraft support
    Servicing
    Loading / Unloading operations

## Slide 10: 2.0 Characteristics of Airport Areas
Aprons: Commercial (Air Carrier)
    Park aircraft
    Board & Deplane passengers
    Baggage, Fueling
    Aircraft servicing

## Slide 11: 2.0 Characteristics of Airport Areas
Aprons: Cargo Apron
  Parked cargo aircraft
  Load/Unload Cargo
  Fuel Aircraft

## Slide 12: 2.0 Characteristics of Airport Areas
Aprons: Hangar Apron
    Temporary parked aircraft
    Maintenance checks
    Can be a diverse Aircraft mix
    Various aircraft types

## Slide 13: 2.0 Characteristics of Airport Areas
Within the Apron, is an Aircraft Stand:
Very Busy, Many functions

## Slide 14: 2.0 Characteristics of Airport Areas
Within the Apron, is an Aircraft Stand:
Very Busy, Many functions

## Slide 15: 2.0 Characteristics of Airport Areas
This section defines the activities and operations on the Airport:
  Landside Areas
    Departure / Arrival Areas
    Walkways from Parking to Terminal
    Roadway systems surrounding the Terminal
    Directional signage
    Secured access points
    Surface parking and garage parking
  Tunnel lighting, under taxiways
  Laser sensitive areas

## Slide 16: 3.0 Visual Issues
Visual issues will be unique to each airport based on operations and layout of the airport.
Visual issues include how lighting design for a task impacts other areas:
The designer must consider the effect of the lighting design on the:
  Airport Geometry
  Control Tower
  Pilot
  Pedestrian and Driver Conflicts (landside)
  Security

## Slide 17: 3.0 Visual Issues
Visual issues for Airport Geometry:
  Approach Areas
  Height restrictions
  Part 77 surfaces

## Slide 18: 3.0 Visual Issues
Visual issues based on Airport Geometry:
  Imaginary Surfaces
  Approach Slopes

## Slide 19: 3.0 Visual Issues
Visual issues for Control Tower:
  Reflected light can be troublesome
  Controllers vision should not be impaired by glare or obtrusive light

## Slide 20: 3.0 Visual Issues
Visual issues for Pilot:
  Approaching Airport
  Rollout

## Slide 21: 3.0 Visual Issues
Visual issues for Pilot:
  Taxiing
  Parking the Aircraft

## Slide 22: 3.0 Visual Issues
Visual issues for Pedestrian and Driver Conflicts (landside):
  Magnitude of pedestrian flow is related to quantity of aircraft arrivals and departures
  Moving and stopped vehicles in the areas
  Distractions and unfamiliarity with services

## Slide 23: 3.0 Visual Issues
Visual issues for Pedestrian and Driver Conflicts (landside):
  This section adapted from ANSI/IES RP-8-14 American National Standard for Roadway Lighting
  All airport “Pedestrian Conflict Areas”
  are classified as “High”

## Slide 24: 3.0 Visual Issues
Visual issues for Security (both airside and landside):
  Maintain security of aircraft, aircraft perimeter
  Consider walkways and pathways
  Parking areas
  Keep line of sight open
  No hard corners/hiding places
  Tree canopies min. of 7ft above ground
  Softscape landscapes kept low
  Safety enhanced when people can see
  each other beyond 30 feet
  (fight or flee)

## Slide 25: 4.0 Design Criteria
This section contains design information for lighting the airport environment. Design Criteria is provided in Tabular form to be used with guidance provided.
  Codes, ordinances or mandates can supersede any of the IES criteria.
  This document does not supersede any government regulation, safety criteria or the Authority Having Jurisdiction
  Guidance Documents exist and designer should be familiar with:
    FAA AC 150/5300-13 Airport Design
    ICAO Aerodrome Manuals
    European Standards
  Lighting design should avoid objectional spill light and glare

## Slide 26: 4.0 Design Criteria
Design Criteria Tables:
Table 1-Airside Areas
  Aprons
  De-Icing areas
  This document does not supersede any government regulation, safety criteria or the Authority

## Slide 27: 4.0 Design Criteria
Design Criteria:
Aircraft stands can accommodate multiple aircraft types, dimensional data and pilots eye position

## Slide 28: 4.0 Design Criteria
Design of poles should minimize glare to pilot. Mounting height of luminaires should be at least 2X the pilots eye position height for largest design aircraft at the stand.

## Slide 29: 4.0 Design Criteria
Design:
  Provide light directed to aircraft stand from two or more directions
  Shadows on the apron can impact efficiencies, goal is to minimize shadows
  Shadows are created when light poles are omitted between aircraft

## Slide 30: 4.0 Design Criteria
Good lighting design:
  Provides uniform lighting on apron
  Decreases shadow on apron
  Minimizes pilot glare
  Light is cutoff outside the area to be illuminated

## Slide 31: 4.0 Design Criteria
Fueling areas:
  Provides increased lighting for loading areas
  Minimizes glare
  Light is cutoff outside the area to be illuminated

## Slide 32: 4.0 Design Criteria
De-icing areas can be located at locations where poles cannot be installed, use of equipment mounted lights may be required.
Coordinate deicing operations:
  Surface height restrictions
  Approach aircraft
  Glare from deice operations

## Slide 33: 4.0 Design Criteria
Design Criteria Tables:
Table 1- Landside Areas
  Departures/arrivals
  Road systems
  Parking
  Landscaped areas
  Vechicle tolls

## Slide 34: 4.0 Design Criteria
Design Criteria:
Landside Areas
  Walkways to/from parking and rental cars
  Illuminate area at least 30 feet around the walkway for security and visual recognition

## Slide 35: 4.0 Design Criteria
Design Criteria:
Roadside / Pedestrian Areas
  Conflict areas to be well illuminated
  Provide luminance of pedestrians for vehicle drivers to visually acquire
  Avoid lights only at cross walks

## Slide 36: 4.0 Design Criteria
Design Criteria Tables:
Other Airside Areas, Industrial areas / Activities on and around an airport are provided in Table 3.
  De-icing vehicle loading areas
  Loading and unloading of fuels and liquids
  Fuel tank fields
  Outdoor electrical equipment

## Slide 37: 5.0 Essential Safety and Security Lighting
This section contains information for safety and security lighting for public egress and safety. Guidance is given for:
  Exit Lighting – To Apron Area from the Building
  Coordinate with the facilities back-up power system:
    Design duration of power outage
    Available power capacity of the standby systems
    Restrike time of HID lamps
    Review with AHJ

## Slide 38: 6.0 Environmental Conditions
This section contains guidance for lighting design with respect for the environment, neighbors and future generations.
  Light Pollution and Light Trespass
  Boundary Limit Concepts
  Lighting Ordinances
  Outdoor Site-Lighting Performance (OSP)
  Leadership in Energy and Environmental Design (LEED)
  Ecological Aspects
  Sustainable Development

## Slide 39: Annex A through I
Annex information is provided from other documents to provide lighting criteria and information:
  Values for Roadways, pedestrian areas
  Field Measurements and performance criteria
  Maintenance Considerations
  Lighting Equipment
  Economic Considerations
  Aviation Glossary
  References
  Suggested Reading
  Lighting Terms
last

## Slide 40: Questions or Comments?
Richard Larivée, P.E., Chair IES RP-37
IESALC recommended practices subcommittee email:
practices@iesalc.org